## Slide 1: Snack Trax
IoT Midterm 1: Smart Room Controller
Phylicia Bediako
July 2025

## Slide 2: Introduction
Team
Project Lead
  Phylicia Bediako
Initial Concept Peer Feedback
  Nicole DeVoe Rogers
  Cesar Silva
  Danny Gallegos
Technical Assistance & Support
  IoT Deep Dive instructors
  IoT Deep Dive Cohort 16
Project Idea & Motivation
  A food storage tracking system inspired by the IoT Deep Dive snack pantry
  Motivated by the fact that the IoT class can request snacks be refilled

## Slide 3: Schematic

## Slide 4: Fritzing

## Slide 5: Introduction
  Wood-encased control panel
  Acrylic scale plate and base
  3D printed inner tray

## Slide 6: Functionality
  Environmental conditions sensor
  BME280 provides real-time temperature and humidity readings
    tempC=bme.readTemperature();
    tempF=(tempC*1.8) +32;
    humidRH=bme.readHumidity();
  Food scale
  HX711 load cell and amp measuring up to 1 kg
    snackScale.set_scale();
    delay(5000);
    snackScale.tare();
    snackScale.set_scale(CALFACTOR);
    weight = snackScale.get_units(SAMPLES);

## Slide 7: Functionality
  Control panel indicator lights
  Three neopixels turn red or green based on status
  OLED
  Shows detailed readings for temperature, humidity, and weight
  Smart device capability
  Connects to smart hue lights and Wemo for room-wide alerts
  Rotary encoder dial adjusts hue light brightness

## Slide 8: Notable Challenges
  Calibrating the load cell
    Reduced size of load cell
  Wiring difficulties with separate sensor/scale and display/control elements
    Consolidated all functions into one control panel
  Determining the right material, sizes, and thickness for the scale plate and base
    Some trial and error led to a thicker acrylic scale plate
    Table saw did not work to cut acrylic, shifted to miter saw/laser cutter method

## Slide 9: Future Steps
  Separate control/display and sensor/scale elements
  Add capability to adjust ideal temperature, humidity, and weight settings using the control panel
  Added “caution” status indicator
  Increased weight capacity
  Customized, snack-specific settings